## Slide 1: JaveOne4Kids 2017
Lego Mindstorms workshop
September 30 2017

## Slide 2: LeJOS
How it works on the EV3
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 3: The Heart of the EV3
TI Sitara AM1808
  ARM9, 300Mhz
64MB RAM / 16MB Flash
Analog to Digital Converter
4 Motor Ports
4 Sensor Ports
Bluetooth / USB
MicroSD
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 4: EV3 Motors
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 5: EV3 Sensors
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 6: Color and Light Sensor
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 7: Ultrasonic Sensor
High frequency
sound waves
Measuring mode Vs Presence Mode
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 8: Infrared Sensor
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 9: Remote Control
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 10: Getting Started with LeJOS
Micro SD Card (> 2GB)
Compatible WIFI adapter
  NetGear WNA1100
  EDIMAX EW-7811Un
Linux (or a Linux VM)
Details here:
Creating Your SD Card
http://sourceforge.net/p/lejos/wiki/Home/
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 11: Windows USB Connection
Step 1: The wrong driver gets installed, so we need to fix this in the Device Manager
Credit to the ev3dev team for the great screen captures and writeup: http://www.ev3dev.org/docs/tutorials/connecting-to-the-internet-via-usb/?tabs-0=windows-7-8
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 12: Windows USB Connection
Step 2: In Device Manager, find your EV3’s RNDIS device. It is under Network Adapters > USB Ethernet/RNDIS Gadget.
Credit to the ev3dev team for the great screen captures and writeup: http://www.ev3dev.org/docs/tutorials/connecting-to-the-internet-via-usb/?tabs-0=windows-7-8
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 13: Windows USB Connection
Step 3: Double-click it and select the Drivers tab. Click Update driver… to change the driver.
Credit to the ev3dev team for the great screen captures and writeup: http://www.ev3dev.org/docs/tutorials/connecting-to-the-internet-via-usb/?tabs-0=windows-7-8
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 14: Windows USB Connection
Step 4: Select Browse my computer for driver software.
Credit to the ev3dev team for the great screen captures and writeup: http://www.ev3dev.org/docs/tutorials/connecting-to-the-internet-via-usb/?tabs-0=windows-7-8
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 15: Windows USB Connection
Step 5: Click Let me pick from a list of device drivers on my computer.
Credit to the ev3dev team for the great screen captures and writeup: http://www.ev3dev.org/docs/tutorials/connecting-to-the-internet-via-usb/?tabs-0=windows-7-8
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 16: Windows USB Connection
Step 6: Uncheck the box that says Show compatible hardware. In the Manufacturer list, pick Microsoft Corporation (in Windows 8, pick Microsoft). In the Network Adapter list, pick Remote NDIS Compatible Device. Then click Next.
Credit to the ev3dev team for the great screen captures and writeup: http://www.ev3dev.org/docs/tutorials/connecting-to-the-internet-via-usb/?tabs-0=windows-7-8
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 17: Windows USB Connection
Step 7: Windows thinks we don’t know what we are doing, but really we do, so click Yes.
Credit to the ev3dev team for the great screen captures and writeup: http://www.ev3dev.org/docs/tutorials/connecting-to-the-internet-via-usb/?tabs-0=windows-7-8
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 18: Windows USB Connection
Step 8: When it is done installing, click Close.
Credit to the ev3dev team for the great screen captures and writeup: http://www.ev3dev.org/docs/tutorials/connecting-to-the-internet-via-usb/?tabs-0=windows-7-8
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 19: Eclipse Setup
Open Eclipse
Go to "Preferences"
Click on leJOS EV3
Change the brick name to the IP address of your brick
  (default is 10.0.1.1)
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 20: Creating a New LeJOS Project
Go to "File" > "New" > "Project…"
Choose a LeJOS EV3 Project
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 21: Create a Class File
Create a new class ("File" > "New" > "Class")
Give it a package (e.g. sample)
Give it a name (e.g. LCDTest)
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 22: Simple LeJOS Application
public class EV3FirstProgram {
public static void main(String[] args) {
LCD.clear();
LCD.drawString("First EV3 Program", 0, 5);
Button.waitForAnyPress();
LCD.clear();
LCD.refresh();
}
}
Slide copied from: http://www.slideshare.net/steveonjava/devoxx4kids-lego-workshop?ref=http://steveonjava.com/java-lego-workshop-4-kids/

## Slide 23: Create and Program Lift

## Slide 24
Build Base

## Slide 25
Build Base

## Slide 26
Reinforce Base

## Slide 27
Construct Pillars
Side View
Top View

## Slide 28
Construct Pillars
Repeat for other side

## Slide 29
Construct Pillars
Repeat for other side

## Slide 30
Construct Pillars
Repeat for other side

## Slide 31
Construct Pillars
Repeat for other side

## Slide 32
Construct Top

## Slide 33
Complete the structure

## Slide 34
Complete the structure

## Slide 35
Construct the lift

## Slide 36
Connect lift and structure
Small thread

## Slide 37
Build mount for pulley motor

## Slide 38
Mount the pulley motor
Make sure to wrap the thread around the motor shaft

## Slide 39: Elevator Wiring
Port A – Pulley Motor
  Pulley motor

## Slide 40: Assembled Elevator
Top View
Side View

## Slide 41: Move the Elevator
public class Elevator {
public static void main(String[] args) {
NXTRegulatedMotor pulleyMotor = Motor.A;
// Move up
pulleyMotor.rotate(360 * 2);
pulleyMotor.rotate(180);
// Move down
pulleyMotor.rotate(-360 * 2);
pulleyMotor.rotate(-180);
}
}

## Slide 42: Trigger with Button
public class Elevator {
public static void main(String[] args) {
NXTRegulatedMotor pulleyMotor = Motor.A;
// Move up
pulleyMotor.rotate(360 * 2);
pulleyMotor.rotate(180);
// Move down
pulleyMotor.rotate(-360 * 2);
pulleyMotor.rotate(-180);
}
}

## Slide 43: Turn off with Light Switch
public class Elevator {
public static void main(String[] args) {
NXTRegulatedMotor pulleyMotor = Motor.A;
// Move up
pulleyMotor.rotate(360 * 2);
pulleyMotor.rotate(180);
// Move down
pulleyMotor.rotate(-360 * 2);
pulleyMotor.rotate(-180);
}
}

## Slide 44: Putting it all together…
Can you write a program that will:
Move up the lift
Move down the lift
Use the button to trigger motion
    If lift is up, it should go down
    If lift is down, it should go up
Exit the program automatically, by using the sensor